## Slide 1: TFLite to Verilog streaming CNN compiler for embedded AI applications andromeda.py + conv2d.v + concatenate.v + replicate.v

## Slide 2: Replicate(), Concatenate(), Add()
https://vision.middlebury.edu/stereo/data/scenes2006/

## Slide 3: Applications
LAD-RCNN:A Powerful Tool for Livestock Face Detection and Normalization
EvConv: Fast CNN Inference on Event Camera Inputs For High-Speed Robot Perception
  Sony Event-based Vision Sensor
CNN-based Methods for Object Recognition with High-Resolution Tactile Sensors
FusionRCNN: LiDAR-Camera Fusion for Two-stage 3D Object Detection
Low-complexity CNNs for Acoustic Scene Classification
Counting Varying Density Crowds Through Density Guided Adaptive Selection CNN and Transformer Estimation
Agricultural Plantation Classification using Transfer Learning Approach based on CNN
Predictive Modeling of Charge Levels for Battery Electric Vehicles using CNN EfficientNet and IGTD Algorithm
A CNN Approach for 5G mmWave Positioning Using Beamformed CSI Measurements

## Slide 4: Target applications
Prediction / parameter estimation from joint sensor data at ~100K samples/sec
  e.g. MLX90640 thermal array, piezo, Hall effect
  app: thermal screening , motor control, equipment monitoring
AI audio processing using multiple microphones/speakers
Advanced multi-camera vision tasks at 100M+ pixels/s
  300+ FPS, 20M+ uncompressed pixel resolution, 10+ cameras, hyperspectral
AI radio using RF baseband IQ samples, MIMO antennas
Replace traditional DSP algorithms with trained deep models
- Performance improvement from using deep model instead of heuristics
- Can learn over time and adapt
- Can automate the implementation of e.g. MATLAB model using imitation learning

## Slide 5: Streaming CNN compiler
model.tflite
FlatBuffers
andromeda.py
--model model.tflite
--clk 100e6
--fps 30
model.v
conv2d.v
conv2d_data.v
conv2d_ctrl.v
model_rom.v
Vivado
Quartus
Raptor
dc_shell
iverilog
VCS
automated tool to compile TFLite model into synthesizable Verilog, using conv2d.v parameterized module
compiler generates parallel code for OCHAN*NSTRIPE MAC operations per layer
Notes: inference only, supports small but useful subset of TFLite (conv2d only, padding='valid', stride={1,2}, activation=RELU)
no external memory required
real time data stream -> real time prediction stream (or feature map)
tool to compile TFLite model into synthesizable Verilog
generated Verilog code is self contained, includes streaming inference and weights
compiler generates parallel code for OCHAN*NSTRIPE MAC operations
compiler generates ROM file with the weights

## Slide 6: Generated Verilog
model.v
conv2d.v
conv2d_data.v
#(ICHAN,OCHAN,NSTRIPE)
S_DATA[ICHAN]
conv2d_data.v
#(ICHAN,OCHAN,NSTRIPE)
conv2d_data.v
#(ICHAN,OCHAN,NSTRIPE)
model_rom.v
model_rom.v
model_rom.v
M_DATA[OCHAN]
CLK
conv2d.v
conv2d.v
conv2d_ctrl.v
#(KHEIGHT,KWIDTH,…)
S_VALID
M_VALID
conv2d_ctrl.v
#(KHEIGHT,KWIDTH,…)
conv2d_ctrl.v
#(KHEIGHT,KWIDTH,…)
RESET
S_ROW, S_COL
M_ROW, M_COL

## Slide 7: Parallel computation of CNN dot products
input feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
output feature vector
[1,1,ochan]
same shape
tensor dot product
parallel ochan
parallel nstripe

## Slide 8
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
TDP RAM
TDP RAM
TDP RAM
weight [OCHAN]
padded stripes [NSTRIPE]
DTYPE*ICHAN
conv2d_data.v : NSTRIPE=3, OCHAN=8
op
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
DTYPE*OCHAN
TDATA
wa,wen
ra
ichan sel
ra
stripe_sel
reg_a
reg_b
reg_z
patch
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
acc
clr

## Slide 9
input data
acc
bias
1: compute dot product
2: add bias
3. multiply by scale
4. shift right with rounding
5. clamp and RELU
s16
weight
s8
*
+
s64
s64
+
scale
u31
CLAMP RELU
s16
output data
*
s96
>>
TFLite 16x8 quantization
u6
shift
rounding right shift

## Slide 10: CNN striped parallel execution
owidth=27*3
stride=1
owidth=14*3
stride=2
ncol
ncol

## Slide 12: Demo
UDP/Ethernet
LiteX SOC
FPGA
streaming CNN
MLX90640
I2C
WB
768x8
768x8
16
WB WR
128
16:1
barrel shifter
CNN
WB RD
reg [7:0] fb[15:0][767:0]
read MLX90640 frame using I2C
read previous prediction and assert seq++
assert reset
copy frame to next fb[15:0]
increment and write chan[3:0]
deassert reset
goto 1

## Slide 13: Demo
0
1
2
pix[9:0]
fb[3:0]
15
2'b00
16'h8001
0
3
1
15
seq_reset
cnn_reset
brl_reset
brl_shift
16'h8000
0
8
data[8:0]
15
FB addr
FB data
CSR 0x80000000
CSR data
0
1
2
pred[2:0]
15
2'b00
16'h8002
0
7
data[8:0]
15
PRED addr
PRED data
4
seq[5:0]
pred seq[5:0] increments every m_tdata_valid
chan0[3:0] selects which physical fb is fed to the CNN input as channel 0
0
2
3

## Slide 14
interleave
concat
[320,320,6]
@120 FPS
[64,64,16]
[64,64,64]
@30 FPS
[16,16,1]
binocular
feature map
multiframe
feature map
NanEye
NanEye
action heatmap
interleave
concat
[1400,1600,6]
@90 FPS
[350,400,16]
@90 FPS
[350,400,64]
@30 FPS
[70,80,1]
binocular
feature map
multiframe
feature map
Mira220
Mira220
action heatmap

## Slide 15
interleave
concat
[1400,1600,6]
@90 FPS
[350,400,16]
@90 FPS
[350,400,64]
@30 FPS
[70,80,1]
binocular
feature map
multiframe
feature map
Mira220
Mira220
action heatmap
interleave
concat
[1400,1600,6]
@90 FPS
[350,400,16]
@90 FPS
[350,400,64]
@30 FPS
binocular
feature map
multiframe
feature map
Mira220
Mira220
P
pan,tilt,zoom
control
T
Z

## Slide 16: High performance demo
MIRA220
XC7VX1140T
USB or Ethernet
1600x1400 RGB @60fps
feature map
classifier heat map
multiframe classifier
classifier heat map (auto PTZ)
multiframe classifier (action recognition)
stereo vision (RGBD)
hyperspectral imaging, feature map based on sensor fusion
line scan image sensor with infinite scrolling
audio analysis using spectrograms https://en.wikipedia.org/wiki/Spectrogram
self supervised visual feature learning https://arxiv.org/pdf/1902.06162.pdf
MIPI CSI-2
DPHY 1.5Gb/s
89x76 mono@60fps

## Slide 17
binocular vision demo - self supervised binocular feature map training
https://en.wikipedia.org/wiki/Binocular_vision
~10 deg vergence angle
~10 cm distance between cameras
predict A given B, B given A, sharing weights
self supervised "pixels to feature map" learning with binocular inputs, multi-frame features
A
B

## Slide 18
https://www.sciencedirect.com/science/article/pii/S0020025522013032
https://www.robots.ox.ac.uk/~vgg/publications/2021/Ge21/ge21.pdf
self supervised egocentric multicamera representations
predict camera A feature map given camera B feature map
predict camera B given camera A, share weights
can extend to more cameras, multiframe feature maps at high frame rate

## Slide 19: References
Research
AoCStream: All-on-Chip CNN Accelerator With Stream-Based Line-Buffer Architecture
https://github.com/Xilinx/finn
A Study on the Intersection of GPU Utilization and CNN Inference
Commercial Edge AI
https://www.nvidia.com/en-us/autonomous-machines/embedded-systems/
https://perceive.io/
TFLite
https://www.tensorflow.org/lite/api_docs
https://arxiv.org/pdf/1712.05877.pdf
https://www.tensorflow.org/lite/performance/quantization_spec
https://www.tensorflow.org/lite/performance/post_training_quantization
https://github.com/tensorflow/tensorflow/blob/92f84571edb98bdb31f1e7b1e23f17bf2c1438e9/tensorflow/lite/kernels/internal/reference/conv.h#L101
https://pypi.org/project/tflite/

## Slide 20: Image Encoder Concept

## Slide 21
parameters
(DRAM)
accelerator
SOC
streaming data
streaming predictions
image
encoder
(SRAM/ROM)
streaming pixels
streaming feature maps
MIMO OFDM
SDR receiver
(SRAM/ROM)
streaming IQ samples
streaming demapped QAM bits
data/task specific inference architectures ("perception components")
general purpose inference architecture ("compute platform")
arbitrary model architecture
arbitrarily large model size
DRAM based model parameters
fixed model architecture
fixed model size
SRAM/ROM based parameters
Notes: wireless MIMO OFDM receiver, replace 50K lines of MATLAB code with 500 lines of Verilog plus a deep model
trend away from general purpose compute platform toward data/task specific component model implementations
image encoder chip can perform different tasks depending on the weights, very flexible for different mass markets
image encoder only performs the front end CNN pyramid, a downstream task will consume feature maps instead of pixels

## Slide 22
image
encoder
(SRAM/ROM)
streaming pixels
feature
map
MIMO OFDM
wireless
(SRAM/ROM)
streaming IQ samples
QAM
soft bits
multimodal LLM
(DRAM)
accelerator
text
payload
FEC DSP
Notes: wireless MIMO OFDM receiver, replace 50K lines of MATLAB code with 500 lines of Verilog plus a deep model
trend away from general purpose compute platform toward data/task specific component model implementations
image encoder chip can perform different tasks depending on the weights, very flexible for different mass markets
image encoder only performs the front end CNN pyramid, a downstream task will consume feature maps instead of pixels

## Slide 23: Technology Strategy
Powerful on-chip models can perform multiple tasks
  for a vision convnet feature map pyramid, 8M weights ~ foundation vision model
  it is feasible to use fixed model arch w/ params on-chip (SRAM or ROM)
  supports image, video, RF and encoder/decoder tasks
Use existing algorithms, implemented in Verilog
  high throughput (>100M samples/s), low latency (<10µs), zero jitter, low power (<2W)
  no new algorithms, leverage TFLite framework, correlated with TFLite reference
  parameterized Verilog code with Python compiler
Notes:   minimize layer variants, "conv2d only", RELU w/o batch norm, skip connections
  params off-chip to on-chip, distributed, aggregate bandwidth
  off-chip weights -> 8 MB * 100 fps = 800 MB/s memory bandwidth
  SRAM/MAC ratio per VGG18 layer, fine grain parallel compute and memory
  avoids access pattern bottlenecks
  CNN have highly parallel and local structure -> pipelined, high MAC utilization
  implement model using dataflow architecture, similar to gnuradio.org
  output channels X number of stripes X pipelined layers -> unexploited parallelism

## Slide 24
Image Encoder
Image Sensors
Robotics
AR/VR
Industrial Measurement
Deep Learning Stack
AMS OSRAM
Onsemi
Google TFLite
eye tracking
AR overlay
integer quantization
Cambrian Robotics
Omron Automation
Cognex
Sensopart
Helmee Imaging
Notes: The image sensor companies have a problem, which is the high data rate of raw pixels over MIPI. Only a handful of SoC platforms can handle MIPI e.g. NVDA Jetson. The result is that the SoC costs more than the image sensor, limiting adoption of embedded vision. The NV image encoder compresses raw pixels into a 30X smaller feature map + thumbnail, which total 78Mb/s and can be transmitted over USB 2.x. This compressed representation can directly drive downstream tasks such as object recognition and localization, image super resolution, and patch embeddings for a multimodal LLM. Horizon tasks include embodied robotic vision, motor control, and MM-LLM executive functions.

## Slide 25: Image Encoder Concept
MIPI
1600x1400 RGB pixels
12 bits/pixel
30 frames/s
= 2.42 Gb/s
USB
[14,18,512] features
16 bits/feature
30 frames/s
= 62 Mb/s
30X
compression
MIPI
[1400,1600,3]
USB2
[14,18,512]
scalable foundation vision CNN with 8M parameters
reconfigurable SRAM-based weights
NV-IE100
500MHz clock
3840 integer MAC units
64Mb SRAM (weights)
20Mb SRAM (rowbuf)
microcontroller
NV-IE100
RGB rescale
[140,160,3]
USB
[140,160,3] thumbnail
8 bits/pixel
30 frames/s
= 16 Mb/s
raw pixels
feature map
thumbnail
Notes: Image Encoder performs the initial convolutional pyramid using a VGG-like 18-layer CNN architecture.
The 8M weight VGG18 architecture is a strong foundation vision model with broad applications.
The image encoder also performs a compression function.
Weights are 8 bits, so 64Mb SRAM (weights) + 20Mb SRAM (row buffers) + standard cell logic

## Slide 26: Reference Board Concept
Mira220
lens mount
MIPI CSI-2
DPHY 1.5Ghz
2 data, 1 clock
IE100
USB2
real time image encoder
compact form factor, USB powered
supports a broad range of applications
low pin count interfaces
includes USB to I2C for configuration
memory map provides access to weights
I2C
NV-IE USB endpoint | M/S
feature pipe | M
thumbnail pipe | M
I2C bridge | S
NV-IE memory map | S

## Slide 27: Execution Plan
chip
reference board
applications
spec
design
DV
PD
tapeout
spec
schematic
layout
build
bringup
image capture
synthetic images
model training
simulated
demo
real time
demo

## Slide 28
randomly populate 16x14 grid locations
label is '0' if empty, '1' if colored ball
224 binary labels
IE100 CNN
1x1 conv, 2x1000 dense, 224 dense
binary crossentropy loss
[1400,1600,3]
[14,18,512]
[224]
1600x1400 RGB images
probabilities
pixels
Receptive field unit test
14 rows
16 columns

## Slide 29
thumbnail gallery of 1600x1400 RGB input images

## Slide 30: Product Planning
Milestone | Dependencies | Status
Concept Commit | PRD/datasheet die size/power estimate preliminary budget/schedule | needed for joint development proposal
Execution Commit | complete program plan to FCS | 
FCS | standard SoC development process | 
PRD Feature | Priority | Schedule
MIPI CSI-2, DPHY RX, 1C 2D, 1.5GHz | P1 | MVP, fastest TTM
[1400,1600,3] input shape (frame) 12 bits/pixel 30 frames/s | P1 | Mira220 RGB
[14,18,512] output shape (feature map) | P1 | 
[140,160,3] output shape (thumbnail) | P1 | 
USB 2.0 PHY, controller | P1 | 

## Slide 31
CNN top
RGB rescaler
AXI-S
I2C controller
sda
scl
clock
data0
data1
AXI-lite
AXI-lite
AXI-S
AXI-lite
AXI-S
AXI-lite
rx
tx
PLL
MIPI
DPHY
CSI-2
AXI-S FIFO
USB
2.x, 480Mb/s
PHY, controller
AXI-S FIFO
AXI-lite master
NV-IE100 top level diagram
Block | Owner
MIPI | 
USB | 
RGB | 
CNN | 
I2C | 
Notes: use box filter for rescaler e.g. https://scholarworks.rit.edu/cgi/viewcontent.cgi?article=10864&context=theses

## Slide 32: Execution Planning
Function | Tasks | Lead
CNN compiler | add level of hierarchy for inferred SRAM add SRAM option to replace weight ROM (SPI config) enhancements and fixes as needed (DAG,TFLite metadata,quantization) | 
RTL design | MIPI CSI-2 RX with DPHY USB PHY and controller CNN top input/output interfaces and FIFO RGB image rescaler and FIFO I2C controller for image sensor configuration | 
Verification (simulation) | End to end unit tests, pixels to predictions Also correlate predictions with TFLite reference interpreter | 
Physical implementation | Standard ASIC flow with 500MHz core clock, 16nm libraries Run initial flat P&R experiment on compiled CNN with 18 layers | 
Tools / Automation | Automate SRAM physical memory compiler for arbitrary size CNN instances | 
Verification (emulation) | Prototype full chip at 200MHz, partition across multiple FPGAs | 
Reference board | Mira220 RGB + NV-IE100, compact fanless form factor, USB powered | 
Applications/Models Documentation FAE Support | Mira220+ Opal Kelly Artix US+ data capture and demo Build reference apps/models e.g facial keypoint detection, image super resolution, support HuggingFace model community | 

## Slide 33: Roadmap
image encoder
Verilog
MIPI
image fusion
feature map history
motion encoder
integrate image fusion and motion encoder into the chip
output feature maps will contain motion information which reduces the frame rate
100M IQ baseband samples/s for wireless sensing and communication e.g. MIMO OFDMA

## Slide 34: NeuVision Robotics Demo Application
Paper | Year | 
A Simple Framework for Contrastive Learning of Visual Representations | 2020 | random crop and rescale
Bootstrap Your Own Latent A New Approach to Self-Supervised Learning | 2020 | positive pairs only
Emerging Properties in Self-Supervised Vision Transformers | 2021 | our baseline method (DINO)
The (Un)Surprising Effectiveness of Pre-Trained Vision Models for Control | 2022 | robot demo
Notes: SimCLR introduced the effectiveness of using random crops from an image for self-supervised representation learning.
BYOL introduced self-supervised learning with positive examples only.
DINO refines BYOL and will serve as our baseline algorithm for self-supervised feature learning for images
For video, transformers may be preferable as sequence processors.
Our initial objective is to demo a real time, pretrained vision model in a robot control setting.

## Slide 35: APPENDIX

## Slide 36: Risks
Risk | Sev | Mitigation
negative effects of integer quantization |  | POR use TFLite signed integer 8b weights, 16b activations Straightforward to switch to 8b/16b floating point as a fallback
no batch normalization or skip connections |  | POR use RELU activations with reduced learning rate Straightforward to support SELU using 64Kx16 SRAM LUT as a fallback
MIPI burstiness due to vertical blanking |  | CNN throughput is specified as a row time, not frame time

## Slide 37: MIPI SoC platforms exceed the cost of the image sensor

## Slide 38: Image Encoder Product Options
NeuVision Product | Model Architecture | Model Weights | Scalability
IE-FPGA | reconfigurable | reconfigurable | <1M weights, <1 TOP, chiplets?
IE-100-RAM | fixed VGG18 | reconfigurable (RAM) | 8M weights, 2 TOP
IE-100-ROM | fixed VGG18 | fixed (ROM) | 8M weights, 2 TOP
Image Encoder performs the initial convolutional pyramid using a VGG-like architecture.
The proposed 8M weight VGG18 architecture is a strong foundation vision model with broad application.
The image encoder also performs a valuable compression function.
Weights are 8 bits, so 64Mb SRAM (weights) + 20Mb SRAM (row buffers) + standard cell logic

## Slide 39
_________________________________________________________________
Layer (type) Output Shape Param #
=================================================================
input_1 (InputLayer) [(None, 1400, 1600, 3)] 0
conv2d (Conv2D) (None, 1398, 1598, 16) 448
conv2d_1 (Conv2D) (None, 698, 798, 16) 2320
conv2d_2 (Conv2D) (None, 696, 796, 16) 2320
conv2d_3 (Conv2D) (None, 694, 794, 32) 4640
conv2d_4 (Conv2D) (None, 346, 396, 32) 9248
conv2d_5 (Conv2D) (None, 344, 394, 32) 9248
conv2d_6 (Conv2D) (None, 342, 392, 64) 18496
conv2d_7 (Conv2D) (None, 170, 195, 64) 36928
conv2d_8 (Conv2D) (None, 168, 193, 64) 36928
conv2d_9 (Conv2D) (None, 166, 191, 128) 73856
conv2d_10 (Conv2D) (None, 82, 95, 128) 147584
conv2d_11 (Conv2D) (None, 80, 93, 128) 147584
conv2d_12 (Conv2D) (None, 78, 91, 256) 295168
conv2d_13 (Conv2D) (None, 38, 45, 256) 590080
conv2d_14 (Conv2D) (None, 36, 43, 256) 590080
conv2d_15 (Conv2D) (None, 34, 41, 512) 1180160
conv2d_16 (Conv2D) (None, 16, 20, 512) 2359808
conv2d_17 (Conv2D) (None, 14, 18, 512) 2359808
=================================================================
Total params: 7,864,704
Trainable params: 7,864,704
Non-trainable params: 0
_________________________________________________________________
proposed VGG-like CNN
uses conv2d layer only
downsample using stride=2
padding=valid
activation nonlinearity=RELU, last layer=None
8 bit integer weights, 16 bit integer activations

## Slide 40: Proposed Image Encoder
MIPI
1600x1400 RGB pixels
12 bits/pixel
110 frames/s
= 8.87 Gb/s
USB
[14,18,512] features
16 bits/feature
110 frames/s
= 0.227 Gb/s
39X compression
MIPI
[1400,1600,3]
USB
[14,18,512]
scalable foundation vision CNN with 8M parameters
reconfigurable SRAM-based weights
NV-IE-MIRA220
500MHz clock
7500 integer MAC units
64Mb SRAM (weights)
20Mb SRAM (rowbuf)
microcontroller
NV-IE-MIRA220
Notes: Image Encoder performs the initial convolutional pyramid using a VGG-like 18-layer CNN architecture.
The 8M weight VGG18 architecture is a strong foundation vision model with broad applications.
The image encoder also performs a compression function.
Weights are 8 bits, so 64Mb SRAM (weights) + 20Mb SRAM (row buffers) + standard cell logic

## Slide 41: Smart Sensor Silicon Segmentation
Sensing
- RISC-V SoC
- Vector ISA
- general purpose connectivity
Vision
- model size versions
e.g. 1M,5M,10M ROM weights
- image fusion versions
e.g. 1,2,3 MIPI inputs
- image resolution versions
e.g. [3840,2160,3], [1600,1400,1]
performance
products
MIPI
USB
NeuVision Image Encoder
Notes: low end can be addressed using RISC-V SoC with vector instructions
high end can be addressed using NeuVision ROM-programmable product line

## Slide 42
collect unlabeled dataset
  synchronized frame capture from multiple image sensors
  synchronized metadata e.g. robot servo angles
self supervised pretraining using unlabeled dataset
  BYOL, DINO
few shot learning using pretrained vision model
  imitation learning for robotics
  classifier for object detection
  image decoder for object segmentation
  patch embeddings for multimodal LLM
data sheet for {100K,1M,5M,20M parameter VGG-like CNN}, {FPGA, ASIC}
  area, ROM area, clock frequency
Notes: Masked Autoencoders As Spatiotemporal Learners
DINOv2: Learning Robust Visual Features without Supervision
Emerging Properties in Self-Supervised Vision Transformers
A Simple Framework for Contrastive Learning of Visual Representations
Bootstrap Your Own Latent A New Approach to Self-Supervised Learning

## Slide 43
Paper | Year | 
A Simple Framework for Contrastive Learning of Visual Representations | 2020 | random crop and rescale
Bootstrap Your Own Latent A New Approach to Self-Supervised Learning | 2020 | positive pairs only
Emerging Properties in Self-Supervised Vision Transformers | 2021 | our baseline method (DINO)
DINOv2: Learning Robust Visual Features without Supervision | 2023 | 
Masked Autoencoders As Spatiotemporal Learners | 2022 | 
The (Un)Surprising Effectiveness of Pre-Trained Vision Models for Control | 2022 | robot demo
Notes: SimCLR introduced the effectiveness of using random crops from an image for self-supervised representation learning.
BYOL introduced self-supervised learning with positive examples only.
DINO refines BYOL and will serve as our baseline algorithm for self-supervised feature learning for images
For video, transformers may be preferable as sequence processors.
Our initial objective is to demo a real time, pretrained vision model in a robot control setting.

## Slide 44
image encoder
Verilog
motion decoder
patch embeddings for multimodal LLM, e.g. SIMVLM
MIPI
depth map
object detection
semantic heatmap
optical flow
image fusion
feature map history
motion encoder
[1120,1280,3]
@110 FPS
[16,19,256]
@10 FPS
1000X compression

## Slide 45
[1120,1280,3]
@110 FPS
[16,19,256]
@110 FPS
image encoder
image sensors
Verilog
CNN
100X compression
image decoder
multimodal LLM, e.g. SIMVLM
MIPI
depth map
object detection
semantic heatmap
patch embeddings
image fusion

## Slide 46
B) parallel output channels
A) parallel vertical stripes
C) parallel layers

## Slide 47
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
TDP RAM
TDP RAM
TDP RAM
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU

## Slide 48
model.tflite
FlatBuffers
Andromeda CNN compiler
--model model.tflite
--clk 200e6
--fps 100
model.v
conv2d.v
concatenate.v
replicate.v
…
model_rom.v
Vivado
Quartus
Raptor
dc_shell
iverilog
VCS
Notes: inference only, supports small but useful subset of TFLite (conv2d only, padding='valid', stride={1,2}, activation=RELU)
no external memory required
real time data stream -> real time prediction stream (or feature map)
tool to compile TFLite model into synthesizable Verilog
generated Verilog code is self contained, includes streaming inference and weights
compiler generates parallel code for OCHAN*NSTRIPE MAC operations
compiler generates ROM file with the weights

## Slide 49: Real time vision IP flow
data collection
"frame burst"
capture to DDR
supervised training
"imitation learning"
use OpenCV brute force algorithms to produce labels
e.g. stereo disparity, optical flow, frequency domain, segmentation
deployment
andromeda.py
conv2d.v
concatenate.v
replicate.v
self-supervised pre-training
+ feature alignment
+ downstream task
collect large, unlabeled, egocentric data set
pretrain using pretext augmentation, contrastive learning e.g. CLIP
align output feature map to downstream task using e.g. linear SVM
converts pixels to feature map
"image encoder"
"foundation vision model"
high speed vision tasks
spatial and temporal fusion
A ConvNet for the 2020s, SIMVLM
can drive multi-model LLM
egocentric
data
model.tflite
model.v
model_rom.v
ongoing data sampling for continuous learning
IP
- using reference datasets and models
- characterize max clock freq, DSP, BRAM, area
- over {input shapes, frame rates, model sizes}
IP characterization

## Slide 50
$1400
$100
Notes: https://www.amazon.com/Yahboom-Raspberry-Omnidirectional-Autopilot-Recognition/dp/B088PRGQJ1/ref=sr_1_24
https://www.amazon.com/Yahboom-Robotic-Raspberry-%EF%BC%88DOFBOT-Without/dp/B08T8XG2J6/ref=sr_1_2
https://www.amazon.com/LewanSoul-Programmable-Feedback-Parameter-Programming/dp/B0793PFGCY

## Slide 51
10b@158MHz
MIPI PHY
KINTEX US XCKU040-2FFVA1156I
ARTIX US+ XCAU25P-2FFVB676E
streaming frame capture
2b@1500MHz
10b@158MHz
2b@1500MHz
MIPI CSI-2
https://www.xilinx.com/products/intellectual-property/jtag_to_axi_master.html
https://docs.xilinx.com/r/en-US/pg232-mipi-csi2-rx/MIPI-CSI-2-Receiver-Subsystem-Product-Guide
https://docs.xilinx.com/v/u/en-US/pg150-ultrascale-memory-ip
https://docs.xilinx.com/r/en-US/pg021_axi_dma/AXI-DMA-Register-Address-Map?section=XREF_38966_AXI_DMA_Simple_DMA
https://docs.xilinx.com/v/u/en-US/ds768_axi_interconnect
format
AXI-S DMA
AXI-S
DDR Memory Controller
S2MM AXI
32b@158MHz
MM2S AXI
AXI Interconnect
control
status
AXILite
AXI-S
ready
interrupt
AXILite
AXILite
JTAG to AXI Master
JTAG
AXILite
I2C Master
AXILite
SCL
SDA
DDR
DRAM
2b@1500MHz
10b@158MHz
[1120,1280,3]
@110fps

## Slide 52
EP address | Type | Bits | Description
0x00 | wire_in | 31:0 | AWADDR
0x01 |  | 31:0 | WDATA
0x02 |  | 31:0 | ARADDR
0x03 |  | 7:0 | AWLEN
0x03 |  | 10:8 | AWSIZE
0x03 |  | 12:11 | AWBURST
0x03 |  | 13 | AWLOCK
0x03 |  | 17:14 | AWCACHE
0x03 |  | 20:18 | AWPROT
0x03 |  | 24:21 | AWQOS
0x04 |  | 3:0 | WSTRB
0x04 |  | 4 | WLAST
0x05 |  | 7:0 | ARLEN
0x05 |  | 10:8 | ARSIZE
0x05 |  | 12:11 | ARBURST
0x05 |  | 13 | ARLOCK
0x05 |  | 17:14 | ARCACHE
0x05 |  | 20:18 | ARPROT
0x05 |  | 24:21 | ARQOS
EP address | Type | Bits | Description
0x20 | wire_out | 0 | AWVALID
0x20 |  | 1 | WVALID
0x20 |  | 2 | BVALID
0x20 |  | 3 | ARVALID
0x20 |  | 4 | RVALID
0x21 |  | 31:0 | RDATA
0x22 |  | 1:0 | BRESP
0x23 |  | 1:0 | RRESP
0x23 |  | 2 | RLAST
EP address | Type | Bits | Description
0x40 | trigger_in | 0 | AWVALID
0x40 |  | 1 | WVALID
0x40 |  | 2 | BREADY
0x40 |  | 3 | ARVALID
0x40 |  | 4 | RREADY
0x40 |  | 5 | global_resetn

## Slide 53
10b@158MHz
MIPI PHY
2b@1500MHz
10b@158MHz
2b@1500MHz
MIPI CSI-2
format
AXI-S
[1120,1280,3]
110fps
convnet model
AXI-S
[480,640,1]
110fps
8b@38MHz
output buffer
USB3
10b@158MHz
2b@1500MHz
10b@158MHz
10b@158MHz
10b@158MHz
MIPI CSI-2
MIPI CSI-2
demo

## Slide 54
https://www.amazon.com/Lottery-Machine-Automatic-Electric-Colorful/dp/B0C1XGSZKQ/ref=sr_1_9?crid=1C4OQX8RFH0P4&keywords=lottery+ping+pong+ball+machine
FPGA
Mira220, IMG.2/SPEED.1/ADC.2
1280x1120/110fps/10b
MIPI CSI-2
stereo disparity
640x480/110fps/8b
USB3
demo concept
M
L
R

## Slide 55
https://www.amazon.com/Lottery-Machine-Automatic-Electric-Colorful/dp/B0C1XGSZKQ/ref=sr_1_9?crid=1C4OQX8RFH0P4&keywords=lottery+ping+pong+ball+machine
FPGA
Mira220, IMG.2/SPEED.1/ADC.2
predict RPLidar 2-D LIDAR map from 3X Mira220 in 360 deg configuration (e.g. Roomba view)
USB3
640x480/110fps/8b
demo concept
1280x1120/110fps/10b
MIPI CSI-2

## Slide 56
LVDS C+2D@1.5GHz
LVDS C+2D@1.5GHz
phase 1
FMC-MIPI
Mira-220
https://docs.arducam.com/Nvidia-Jetson-Camera/type-and-pinout-mipi-csi-2/

## Slide 57
channel interleave
[1400,1600,2]
@90 FPS
Mira220
Mira220
capture buffer
MIPI synchronize deserialize
KINTEX UltraScale XCKU040-2FFVA1156I
phase 1
AXI-S
UDP
MII
udp/eth/mii

## Slide 58
channel interleave
[1400,1600,2]
@90 FPS
[82,95,64]
@90 FPS
self supervised pretrained image encoder
Mira220
Mira220
[82,95,1]
@90 FPS
heat map
phase 2
pretrain using self-supervised pretext tasks on unlabeled data
LR eye swap, predict LR vs RL
LR time shift, predict L[t]R[t] vs L[t-1]R[t] vs L[t]R[t-1]
AXI-S

## Slide 59: Sensing platform
Silicon vision and sensing platform for next generation robotics
  target next generation robotics based on multimodal LLM technology
  the image encoder socket is the first stage in a multimodal LLM e.g. CLIP
  foundation/backbone vision models encode raw pixels into a compressed feature map
  domain specific FPGA enables low latency "pixels to features" at sensor speed
  extends to 360-degree vision, hyperspectral, video, tactile sensors, audio, RF
Strategy
  Open software
  Optimized FPGA silicon initially targeting the emerging image encoder socket
  Scale using chiplets
  Partner with image sensor, robotics ecosystems
Execution
  TF to Verilog demo, real time CNN inference at high resolution and frame rate
  demonstrate vision model using self supervised pretraining on egocentric image data

## Slide 60
Mira220
RPLidar
channel interleave
[1400,1600,4]
@90 FPS
[170,195,1]
@90 FPS
supervised training
predict overhead Lidar view from 4xMira220
Mira220
AXI-S
https://www.slamtec.ai/#
CNN

## Slide 61
channel interleave
[1400,1600,2]
@90 FPS
Mira220
Mira220
capture buffer
LiteX SoC
uart
i2c
ethernet
MIPI synchronize deserialize
KINTEX UltraScale XCKU040-2FFVA1156I
wb
phase 1
AXI-S

## Slide 63
https://www.terasic.com.tw/cgi-bin/page/archive.pl?Language=English&CategoryNo=142&No=1295#contents
https://www.xilinx.com/products/boards-and-kits/1-so55i9.html

## Slide 64: FPGA Compute Platform
Vision
  FPGA as a flexible compute platform
    embedded AI, edge and cloud applications, GPU alternative
Strategy
  GPT-friendly open IP library
  GPT-automated development flow
    Raptor, HW/SW co-design (CUDA, RTOS)
  GPT-assisted dataflow algorithm implementation
    graph based computation for deep models (CNN, Transformer)
      TF to Verilog
    traditional DSP pipelines (vision, RF)
      MATLAB to Verilog
    multiple architectures (training accelerators, embedded streaming inference)
  Compute-optimized FPGA silicon product line
Execution
  "hello world" TF to Verilog demo (embedded real time edge inference)

## Slide 65: Parallel computation of CNN dot products
input feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
output feature vector
[1,1,ochan]
same shape
tensor dot product
parallel ochan
parallel nstripe

## Slide 66: Backup

## Slide 67
input data
acc
bias
1: compute dot product (s9*s9+s32)
2: add bias (s32+s32)
3. multiply by scale (s32*s32)
4. shift right >>31
5. clamp to s9 bits and RELU
s9
weight
s8
*
+
s32
s32
+
scale M
s32
CLAMP RELU
s9
output data
*
s64
>>31
TFLite int8 quantization

## Slide 68
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
TDP RAM
weight [OCHAN]
DTYPE*ICHAN
conv2d_data.v : NSTRIPE=3, OCHAN=8
op
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
DTYPE*OCHAN
wa,wen
ra
ichan sel
ra
stripe_sel
reg_a
reg_b
reg_z
patch
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
acc
clr

## Slide 69
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
TDP RAM
weight [OCHAN]
DTYPE*ICHAN
conv2d_data.v : NSTRIPE=3, OCHAN=8
op
MAC
DTYPE*OCHAN
wa,wen
ra
ichan sel
ra
stripe_sel
reg_a
reg_b
reg_z
patch
ALU
acc
clr

## Slide 70
fill row of
padded stripes
from previous
layer
compute NSTRIPE*OCHAN parallel
dot products, quant scale, RELU
stride through input row data
trow
tdot
(owidth/nstripe)∙tdot < trow
serialize nstripe features over
output TDATA*OCHAN
nstripe ∙ tclk < tdot
ndata = # of input features since TLAST (for current layer)
stripe = ndata % istripe

## Slide 71
owidth=27*3
stride=1
owidth=14*3
stride=2
col
row
ncol
ncol

## Slide 72
_________________________________________________________________
Layer (type) Output Shape Param #
=================================================================
conv2d (Conv2D) (None, 2158, 3838, 8) 224
conv2d_1 (Conv2D) (None, 1078, 1918, 8) 584
conv2d_2 (Conv2D) (None, 1076, 1916, 16) 1168
conv2d_3 (Conv2D) (None, 537, 957, 16) 2320
conv2d_4 (Conv2D) (None, 535, 955, 32) 4640
conv2d_5 (Conv2D) (None, 267, 477, 32) 9248
conv2d_6 (Conv2D) (None, 265, 475, 32) 9248
conv2d_7 (Conv2D) (None, 132, 237, 32) 9248
conv2d_8 (Conv2D) (None, 130, 235, 32) 9248
conv2d_9 (Conv2D) (None, 64, 117, 32) 9248
conv2d_10 (Conv2D) (None, 62, 115, 32) 9248
conv2d_11 (Conv2D) (None, 30, 57, 32) 9248
conv2d_12 (Conv2D) (None, 28, 55, 32) 9248
conv2d_13 (Conv2D) (None, 13, 27, 32) 9248
conv2d_14 (Conv2D) (None, 11, 25, 16) 4624
conv2d_15 (Conv2D) (None, 5, 12, 16) 2320
conv2d_16 (Conv2D) (None, 3, 10, 8) 1160
conv2d_17 (Conv2D) (None, 1, 4, 8) 584
flatten (Flatten) (None, 32) 0
=================================================================
Total params: 100,856
Trainable params: 100,856
Non-trainable params: 0
_________________________________________________________________
+----------+-------+---------------------+
| Ref Name | Used | Functional Category |
+----------+-------+---------------------+
| LUT6 | 18400 | LUT |
| FDRE | 12853 | Flop & Latch |
| MUXF7 | 5218 | MuxFx |
| RAMD64E | 2112 | Distributed Memory |
| RAMB36E1 | 1851 | Block Memory |
| CARRY4 | 1568 | CarryLogic |
| LUT4 | 1517 | LUT |
| DSP48E1 | 1032 | Block Arithmetic |
| LUT5 | 807 | LUT |
| LUT2 | 249 | LUT |
| FDSE | 146 | Flop & Latch |
| LUT1 | 131 | LUT |
| LUT3 | 117 | LUT |
| OBUF | 66 | IO |
| IBUF | 26 | IO |
| MUXF8 | 15 | MuxFx |
| OBUFT | 1 | IO |
| BUFG | 1 | Clock |
+----------+-------+---------------------+
t3.py (4K video @30fps)

## Slide 73
rliston@uscomputefe1:~/andromeda$ python3 andromeda.py --model t3 --fps 30
numpy 1.23.5
Namespace(model='t3', clk=500000000.0, fps=30.0, tdata=8)
layer 0 nstripe 14 stride 1 sdepth 3291 wdepth 31 rate 5.375e+10 nmac 108 shapes [ 1 2160 3840 3] [ 1 2158 3838 8] [8 3 3 3] [8]
layer 1 nstripe 9 stride 2 sdepth 17057 wdepth 76 rate 3.578e+10 nmac 72 shapes [ 1 2158 3838 8] [ 1 1078 1918 8] [8 3 3 8] [8]
layer 2 nstripe 9 stride 1 sdepth 6819 wdepth 76 rate 7.146e+10 nmac 143 shapes [ 1 1078 1918 8] [ 1 1076 1916 16] [16 3 3 8] [16]
layer 3 nstripe 5 stride 2 sdepth 30656 wdepth 148 rate 3.562e+10 nmac 72 shapes [ 1 1076 1916 16] [ 1 537 957 16] [16 3 3 16] [16]
layer 4 nstripe 5 stride 1 sdepth 12249 wdepth 148 rate 7.104e+10 nmac 143 shapes [ 1 537 957 16] [ 1 535 955 32] [32 3 3 16] [32]
layer 5 nstripe 3 stride 2 sdepth 50933 wdepth 292 rate 3.532e+10 nmac 71 shapes [ 1 535 955 32] [ 1 267 477 32] [32 3 3 32] [32]
layer 6 nstripe 3 stride 1 sdepth 20352 wdepth 292 rate 3.521e+10 nmac 71 shapes [ 1 267 477 32] [ 1 265 475 32] [32 3 3 32] [32]
layer 7 nstripe 1 stride 2 sdepth 76000 wdepth 292 rate 8.700e+09 nmac 18 shapes [ 1 265 475 32] [ 1 132 237 32] [32 3 3 32] [32]
layer 8 nstripe 1 stride 1 sdepth 30336 wdepth 292 rate 8.649e+09 nmac 18 shapes [ 1 132 237 32] [ 1 130 235 32] [32 3 3 32] [32]
layer 9 nstripe 1 stride 2 sdepth 37600 wdepth 292 rate 2.112e+09 nmac 5 shapes [ 1 130 235 32] [ 1 64 117 32] [32 3 3 32] [32]
layer 10 nstripe 1 stride 1 sdepth 14976 wdepth 292 rate 2.070e+09 nmac 5 shapes [ 1 64 117 32] [ 1 62 115 32] [32 3 3 32] [32]
layer 11 nstripe 1 stride 2 sdepth 18400 wdepth 292 rate 4.928e+08 nmac 1 shapes [ 1 62 115 32] [ 1 30 57 32] [32 3 3 32] [32]
layer 12 nstripe 1 stride 1 sdepth 7296 wdepth 292 rate 4.728e+08 nmac 1 shapes [ 1 30 57 32] [ 1 28 55 32] [32 3 3 32] [32]
layer 13 nstripe 1 stride 2 sdepth 8800 wdepth 292 rate 1.064e+08 nmac 1 shapes [ 1 28 55 32] [ 1 13 27 32] [32 3 3 32] [32]
layer 14 nstripe 1 stride 1 sdepth 3456 wdepth 292 rate 4.852e+07 nmac 1 shapes [ 1 13 27 32] [ 1 11 25 16] [16 3 3 32] [16]
layer 15 nstripe 1 stride 2 sdepth 2000 wdepth 148 rate 4.752e+06 nmac 1 shapes [ 1 11 25 16] [ 1 5 12 16] [16 3 3 16] [16]
layer 16 nstripe 1 stride 1 sdepth 768 wdepth 148 rate 2.074e+06 nmac 1 shapes [ 1 5 12 16] [ 1 3 10 8] [ 8 3 3 16] [8]
layer 17 nstripe 1 stride 2 sdepth 400 wdepth 76 rate 1.296e+05 nmac 1 shapes [ 1 3 10 8] [1 1 4 8] [8 3 3 8] [8]
total stripe RAM bits 147841520
total weight RAM bits 816832
total required MAC units 733
total used MAC units 1032
rliston@uscomputefe1:~/andromeda$
andromeda.py log file

## Slide 74
3. Memory
---------
+-------------------+------+-------+------------+-----------+-------+
| Site Type | Used | Fixed | Prohibited | Available | Util% |
+-------------------+------+-------+------------+-----------+-------+
| Block RAM Tile | 1851 | 0 | 0 | 1880 | 98.46 |
| RAMB36/FIFO* | 1851 | 0 | 0 | 1880 | 98.46 |
| RAMB36E1 only | 1851 | | | | |
| RAMB18 | 0 | 0 | 0 | 3760 | 0.00 |
+-------------------+------+-------+------------+-----------+-------+
* Note: Each Block RAM Tile only has one FIFO logic available and therefore can accommodate only one FIFO36E1 or one FIFO18E1. However, if a FIFO18E1 occupies a Block RAM Tile, that tile can still accommodate a RAMB18E1
4. DSP
------
+----------------+------+-------+------------+-----------+-------+
| Site Type | Used | Fixed | Prohibited | Available | Util% |
+----------------+------+-------+------------+-----------+-------+
| DSPs | 1032 | 0 | 0 | 3360 | 30.71 |
| DSP48E1 only | 1032 | | | | |
+----------------+------+-------+------------+-----------+-------+
t3.py (4K video @30fps)

## Slide 75: Target applications
high speed, low latency inference at the edge
  ex: 3840x2160 @100 fps image classification for industrial applications
  process raw uncompressed pixels directly from sensor (e.g. HDMI,MIPI)
  hyperspectral image sensors, RF IQ baseband, 300+ frames/s
inference only, supports small but useful subset of TFLite (conv2d only, padding='valid', stride={1,2}, activation=RELU)
no external memory required
real time data stream -> real time prediction stream (or feature map)
tool to compile TFLite model into synthesizable Verilog
generated Verilog code is self contained, includes streaming inference and weights
compiler generates parallel code for OCHAN*NSTRIPE MAC operations
compiler generates ROM file with the weights

## Slide 76
TDP RAM
TDP RAM
TDP RAM
padded stripes [NSTRIPE]
TDATA
TDATA*ICHAN
TDATA
conv2d_data.v
NSTRIPE=3, OCHAN=8
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
TDATA*OCHAN
TDATA
wa,we
ra
ichan sel
stripe_sel
reg_a
reg_b
reg_x
patch
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
acc
clr
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
weight [OCHAN]
ra
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
bias [OCHAN]
scale M0 [OCHAN]
ra
reg_c
reg_d
acc

## Slide 77
input data
output zeropoint
acc
bias
1: compute dot product (8*8+32)
2: add bias (32+32)
3. multiply by M0 scale (32*32)
4. shift right 31 bits with round
5. clamp to 8 bits + RELU
u8
input zeropoint
u8
-
weight
s8
*
+
s8
s32
s32
+
scale M0
u32
*
>> 31
u8
+
CLAMP
8
output data

## Slide 78
nstripes=1
nstripes=3
nstripes=15

## Slide 80
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
TDP RAM
TDP RAM
TDP RAM
weights [OCHAN]
padded stripes [NSTRIPE]
TDATA
TDATA*ICHAN
TDATA
conv2d_data.v : NSTRIPE=3, OCHAN=8
opcode, args
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
TDATA*OCHAN
TDATA
wa,we
ra
ichan sel
ra
stripe_sel
reg_a
reg_b
reg_z
patch

## Slide 81
ROM
ROM
ROM
ROM
ROM
ROM
ROM
ROM
TDP RAM
TDP RAM
TDP RAM
weights [OCHAN]
padded stripes [NSTRIPE]
TDATA
TDATA*ICHAN
TDATA
conv2d_dp.v : NSTRIPE=3, OCHAN=8
opcode, args
TDATA = {int8, bfloat16}
ICHAN = {1..256}
OCHAN = {1..256}
NSTRIPE = {1..64}
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
DSP
TDATA*OCHAN
TDATA
wa,we
ra
ichan sel
ra
stripe_sel
reg_a
reg_b
reg_z
patch
+----------+------+---------------------+
| FDRE | 3735 | Flop & Latch |
| LUT6 | 1634 | LUT |
| LUT4 | 695 | LUT |
| CARRY4 | 586 | CarryLogic |
| DSP48E1 | 510 | Block Arithmetic |
| RAMB18E1 | 181 | Block Memory |
| LUT2 | 177 | LUT |
| RAMB36E1 | 105 | Block Memory |
| OBUF | 82 | IO |
| LUT1 | 64 | LUT |
| LUT3 | 54 | LUT |
| FDSE | 39 | Flop & Latch |
| LUT5 | 24 | LUT |
| IBUF | 10 | IO |
| FDCE | 6 | Flop & Latch |
| OBUFT | 1 | IO |
| BUFG | 1 | Clock |
+----------+------+---------------------+

## Slide 82: andromeda.py streaming CNN compiler
model.tflite
FlatBuffers
andromeda.py
--model model
--clk 500e6
--fps 30
model.v
conv2d.v
conv2d_dp.v
conv2d_ctrl.v
model_weights.v
Vivado
Quartus
Raptor
dc_shell
iverilog
VCS
automated tool to compile TFLite model into synthesizable Verilog
compiler generates parallel code for OCHAN*NSTRIDE MAC operations per layer

## Slide 83: Streaming CNN Verilog Hierarchy
model.v
conv2d.v
conv2d_ctrl.v
conv2d_dp.v
#(ICHAN,OCHAN,NSTRIPE)
weight_rom.v
TVALID,TLAST
TREADY
TDATA
conv2d_ctrl.v
conv2d_dp.v
#(ICHAN,OCHAN,NSTRIPE)
weight_rom.v
conv2d_ctrl.v
conv2d_dp.v
#(ICHAN,OCHAN,NSTRIPE)
weight_rom.v
TVALID,TLAST
TREADY
TDATA
CLK
conv2d.v
conv2d.v
TVALID,TLAST
TREADY
TDATA
(AXI-S)
(AXI-S)

## Slide 84: Streaming CNN Verilog Hierarchy
model.v
conv2d.v
conv2d_ctrl.v
conv2d_dp.v
#(ICHAN,OCHAN,NSTRIPE)
weight_rom.v
TVALID
TLAST
TDATA
conv2d_ctrl.v
conv2d_dp.v
#(ICHAN,OCHAN,NSTRIPE)
weight_rom.v
conv2d_ctrl.v
conv2d_dp.v
#(ICHAN,OCHAN,NSTRIPE)
weight_rom.v
TVALID
TLAST
TDATA
CLK
conv2d.v
conv2d.v

## Slide 85
https://arxiv.org/pdf/1712.05877.pdf
https://www.tensorflow.org/lite/performance/quantization_spec#int8_quantized_operator_specifications
requirements for TFLite quant:
saturating 8*8+32 bit MAC
rounding-to-nearest right-shift
https://en.wikipedia.org/wiki/Wafer-scale_integration
https://en.wikipedia.org/wiki/Cerebras
https://arxiv.org/pdf/2112.07571.pdf

## Slide 86: CNN dot product using FPGA
BRAM
BRAM
stripes
weights

## Slide 87: CNN dot product using FPGA
BRAM
BRAM
row buffer
weights

## Slide 88
MAC
ichan*int8
TDATA
weights
RAM
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
RAM
rowbuf
ochan
1
int8
int8
int8
ochan*int8
TDATA
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 89
MAC
ichan*int8
TDATA
weights
RAM
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
RAM
rowbuf
ochan
1
int8
int8
int8
ochan*int8
TDATA
RAM
RAM
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 90
MAC
ichan*int8
TDATA
weights
RAM
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
RAM
rowbuf
ochan
1
int8
int8
int8
ochan*int8
TDATA
RAM
RAM
MAC*ochan
int8
MAC*ochan
int8
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 91
ochan*int8
TDATA

## Slide 92: CNN dot product using FPGA
feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
feature vector
[1,1,ochan]
same shape
dot product
BRAM
BRAM
row buffer
weights

## Slide 93
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
rowbuf
TDATA
weights
RAM
RAM m
RAM
RAM
RAM
RAM
RAM n
RAM
data path interface
n * rowbuf.wa, we
n * rowbuf.ra
n * rowbuf.ra_adjacent
n * rowbuf.muxsel
m * weights.ra
mac_clear, mac_load
(m=ochan)
RELU
TDATA
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 94
ichan MAC
MAC
MAC
rowbuf
TDATA
shape=[chunk]
dtype=int8
weights
RAM
RAM m
RAM
BRAM
data path interface
n * rowbuf.wa, we
n * rowbuf.ra
n * rowbuf.ra_adjacent
n * rowbuf.muxsel
m * weights.ra
mac_clear, mac_load
(m=ochan)
serialize flattened tensor
send tensor over TDATA in S*dtype size chunks
write and read BRAM in S*dtype size chunks
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 95
fps | 289 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
width | 728 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
height | 544 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
channels | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
clk | 500,000,000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
layer | iwidth | iheight | ichan | stride | kheight | kwidth | owidth | oheight | ochan | patches/s | MAC/patch | MAC/s | required MAC | row buffer words | weight words | n | n*m | rowbuf depth
1 | 728 | 544 | 3 | 1 | 3 | 3 | 726 | 542 | 32 | 114,453,248 | 864 | 98,887,606,272 | 198 | 6,552 | 864 | 7 | 224 | 936
2 | 726 | 542 | 32 | 2 | 3 | 3 | 362 | 270 | 32 | 28,246,860 | 9,216 | 260,323,061,760 | 521 | 69,696 | 9,216 | 17 | 544 | 4,100
3 | 362 | 270 | 32 | 1 | 3 | 3 | 360 | 268 | 32 | 27,882,720 | 9,216 | 256,967,147,520 | 514 | 34,752 | 9,216 | 17 | 544 | 2,044
4 | 360 | 268 | 32 | 2 | 3 | 3 | 179 | 133 | 32 | 6,880,223 | 9,216 | 63,408,135,168 | 127 | 34,560 | 9,216 | 4 | 128 | 8,640
5 | 179 | 133 | 32 | 1 | 3 | 3 | 177 | 131 | 32 | 6,701,043 | 9,216 | 61,756,812,288 | 124 | 17,184 | 9,216 | 4 | 128 | 4,296
6 | 177 | 131 | 32 | 2 | 3 | 3 | 88 | 65 | 32 | 1,653,080 | 9,216 | 15,234,785,280 | 31 | 16,992 | 9,216 | 1 | 32 | 16,992
7 | 88 | 65 | 32 | 1 | 3 | 3 | 86 | 63 | 32 | 1,565,802 | 9,216 | 14,430,431,232 | 29 | 8,448 | 9,216 | 1 | 32 | 8,448
8 | 86 | 63 | 32 | 2 | 3 | 3 | 42 | 31 | 32 | 376,278 | 9,216 | 3,467,778,048 | 7 | 8,256 | 9,216 | 1 | 32 | 8,256
9 | 42 | 31 | 32 | 1 | 3 | 3 | 40 | 29 | 32 | 335,240 | 9,216 | 3,089,571,840 | 7 | 4,032 | 9,216 | 1 | 32 | 4,032
10 | 40 | 29 | 32 | 2 | 3 | 3 | 19 | 14 | 32 | 76,874 | 9,216 | 708,470,784 | 2 | 3,840 | 9,216 | 1 | 32 | 3,840
11 | 19 | 14 | 32 | 1 | 3 | 3 | 17 | 12 | 32 | 58,956 | 9,216 | 543,338,496 | 2 | 1,824 | 9,216 | 1 | 32 | 1,824
12 | 17 | 12 | 32 | 2 | 3 | 3 | 8 | 5 | 32 | 11,560 | 9,216 | 106,536,960 | 1 | 1,632 | 9,216 | 1 | 32 | 1,632
13 | 8 | 5 | 32 | 1 | 3 | 3 | 6 | 3 | 32 | 5,202 | 9,216 | 47,941,632 | 1 | 768 | 9,216 | 1 | 32 | 768
14 | 6 | 3 | 32 | 2 | 3 | 3 | 2 | 1 | 32 | 578 | 9,216 | 5,326,848 | 1 | 576 | 9,216 | 1 | 32 | 576
15 | 2 | 1 | 32 | 1 | 3 | 3 | 0 | -1 | 32 | - | 9,216 | - | - | 192 | 9,216 | - | - | #DIV/0!
 |  |  |  |  |  |  |  |  |  |  |  | 778,976,944,128 | 1,565 | 209,304 | 129,888 | 58 | 1,856 | 
write incoming features from AXI-S to rowbuf[]
when a compete row of patches has arrived, begin computing dot products per-inputslice per-chanout
n*m features will complete simultaneously, write them sequentially into the reorder buffer

## Slide 96
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*o
rowbuf
TDATA
weights
RAM
RAM o
RAM
RAM
RAM
RAM
RAM n
RAM
data path interface
n * rowbuf.wa, we
n * rowbuf.ra
n * rowbuf.ra_adjacent
n * rowbuf.muxsel
m * weights.ra
mac_clear, mac_load
(o=ochan)
RELU
RAM
n:1
RAM
RAM
RAM m
o:1
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 97
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
rowbuf
TDATA
weights
RAM
RAM m
RAM
RAM
RAM
RAM
RAM n
RAM
data path interface
n * rowbuf.wa
n * rowbuf.ra
n * rowbuf.ra_adjacent
n * rowbuf.muxsel
m * weights.ra
mac_clear, mac_load
(m=ochan)
RELU
TDATA
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 98: CNN dot product using FPGA
feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
feature vector
[1,1,ochan]
same shape
dot product
conv2d.v
BRAM
BRAM
row buffer
weights
AXI-S
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
RAM
RAM m
RAM
RAM
RAM
RAM
RAM n
RAM
AXI-S

## Slide 99
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
TDATA
RAM
reorder
TVALID
TLAST
TREADY
rowbuf
TDATA
weights
RAM
RAM m
RAM
TVALID
TLAST
TREADY
RAM
RAM
RAM
RAM n
RAM
RELU
data path interface
n * rowbuf.wa
n * rowbuf.ra
m * weights.ra
mac_clear, mac_load
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 100
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
TDATA
RAM
reorder
TVALID
TLAST
TREADY
rowbuf
TDATA
weights
RAM
RAM m
RAM
RAM
RAM
RAM
RAM n
RAM
RELU
data path interface
n * rowbuf.wa
n * rowbuf.ra
m * weights.ra
mac_clear, mac_load
1-32 chunk of int8
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
always use m=ochan as a simplification
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 101: CNN dot product using FPGA
feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
feature vector
[1,1,ochan]
same shape
dot product
conv2d.v
BRAM
BRAM
row buffer
weights
AXI-S
layer 1
layer 2
layer n
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
RAM
RAM
RAM m
RAM
RAM
RAM
RAM
RAM n
RAM
AXI-S

## Slide 102
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 104: CNN dot product using FPGA
feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
feature vector
[1,1,ochan]
same shape
dot product
BRAM
BRAM
DSP
18
conv2d.v
BRAM
BRAM
row buffer
weights
18
AXI-S
AXI-S
layer 1
layer 2
layer n

## Slide 105
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
TDATA
RAM
reorder
TVALID
TLAST
TREADY
rowbuf
TDATA
weights
RAM
RAM m
RAM
TVALID
TLAST
TREADY
RAM
RAM
RAM
RAM n
RAM
RELU
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each RAM stores complete input patches (input activations in the rowbuf and per-output channel weights)
m <= output channels
each MAC computes a complete dot product to produce an output feature
parallelism comes from 1) row buffer stripes are computed in parallel, patch by patch and 2) output feature vector channels are computed in parallel
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining, striping
TDATA is int8 or float16
compute dot products of each input rowbuf stripe in parallel

## Slide 106
row buffer
TDATA
weights
RAM
RAM m
4Kx8 RAM
8*8+32 MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
TDATA
BRAM
RAM
reorder buffer
TVALID
TLAST
TREADY
TVALID
TLAST
TREADY
4Kx8 RAM
RAM
RAM
RAM n
RAM
Notes: stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each BRAM stores complete patches (input activations and weights)
circular row buffer
each BRAM contains an overlapped vertical slice of the row buffer, contains complete patches, stripmining

## Slide 107
RAM
RAM m
4Kx8 RAM 1
input buffer
TDATA
weights
RAM
RAM
RAM n
RAM
4Kx8 RAM 1
8*8+32 MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
stripe input activations across input buffer BRAMs
compute n*m dot products in parallel
each BRAM stores complete patches (input activations and weights)
TDATA
BRAM
input buffer
each BRAM contains an overlapped
vertical slice of the row buffer,
contains complete patches
stripmining
RAM
reorder buffer
TVALID
TLAST
TREADY
TVALID
TLAST
TREADY

## Slide 108
RAM 2
RAM m
RAM 1
input buffer
TDATA
model parameters
RAM 2
RAM 3
RAM n
RAM 4
RAM 1
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC n*m
MAC
input buffer
each BRAM contains an overlapped
vertical slice of the row buffer,
contains complete patches
BRAM
compute n*m dot products in parallel

## Slide 109
URAM 2
URAM m
URAM 1
URAM 2
URAM m
BRAM 1
input buffer
TDATA
TDATA
model parameters
FPU
FPU
BRAM 2
BRAM 3
BRAM n
BRAM 4
URAM 1
MAC
MAC
MAC

## Slide 110
TFLite to MLIR, starting with Conv2D

## Slide 111
AXI-S
AXI-S
AXI-S
FPU
32
32
32
URAM
32
AXI-S
flowgraph tile
circular buffer
model
dot product
32
32
shape @rate
[2160,3840,64]
[24,32,1]
@30Hz

## Slide 112
AXI-S
AXI-S
AXI-S
FPU
32
32
32
URAM
32
AXI-S
flowgraph tile
circular buffer
model
dot product
32
32
shape @rate
[24,32,1] @30Hz
[24,32,1] @30Hz

## Slide 113
AXI-S
AXI-S
AXI-S
FPU
32
32
32
URAM
32
AXI-S
flowgraph tile
fifo
model
dot product
32
32
32
32
32
AXI-S
AXI-S
shape @rate
[24,32,1] @30Hz

## Slide 114
AXI-S
AXI-S
AXI-S
FPU
32
32
32
URAM
32
AXI-S
flowgraph tile
fifo
model
CLB
dot product
32
32

## Slide 115
AXI-S0
AXI-SI
AXI-S2
FPU
32
32
32
URAM
32
AXI-S
AI tile
deinterleave
fifo
model
CLB
dot product
32
32

## Slide 116
URAM 2
URAM m
URAM 1
URAM 2
URAM m
BRAM 1
input buffer
TDATA
TDATA
model parameters
FPU
FPU
BRAM 2
BRAM 3
BRAM n
BRAM 4

## Slide 117
conv2d.v is a Tensorflow compatible CNN layer implementation
Each layer in the model is evaluated in parallel using pipelining
Weights are stored in on-chip BRAM for high performance
Can be used stand alone or as a front end to a larger model
Real time classification demo for Gemini
- Code complete, runs at 200MHz using Artix-7/Vivado
- Next step is functional verification using MNIST

## Slide 118: conv2d.v

## Slide 119: Objectives
initially target Gemini fabric
high throughput, low latency deep model evaluation
efficiently utilize FPGA BRAM and DSP resources
package as a parameterized, reusable IP
AXI-S
18
conv2d.v
conv2d.v
conv2d.v
AXI-S
18
conv2d.v

## Slide 120: CNN primitive operation
feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
feature vector
[1,1,ochan]
same shape
tensor dot product

## Slide 121: CNN primitive operation
feature patch
[3,3,ichan]
weights
[ochan,3,3,ichan]
feature vector
[1,1,ochan]
same shape
tensor dot product

## Slide 122: CNN dot product using FPGA
BRAM
BRAM
stripes
weights

## Slide 123
DSP
TDATA
acc
18
RELU
TDATA
18
BRAM
row buffer
weights
BRAM
Sequential implementation

## Slide 124
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM m
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM m
18x1K BRAM 1
row buffer
TDATA
TDATA
n=(iwidth*3*ichan)/1K
m=(3*3*ichan)/1K
ndsp=ochan
ex: ichan=3,ochan=16,iwidth=768
ex: ichan=256,ochan=256,iwidth=192
ochan
Parallel implementation
weights
DSP
DSP
18x1K BRAM 2
18x1K BRAM 3
18x1K BRAM n
18x1K BRAM 4

## Slide 125
URAM 1
URAM 2
URAM m
URAM 1
URAM 2
URAM m
BRAM 1
input buffer
TDATA
TDATA
model parameters
FPU
FPU
BRAM 2
BRAM 3
BRAM n
BRAM 4

## Slide 126
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM m
DSP 1
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM m
18x1K BRAM 1
row buffer
chained
accumulator
TDATA
TDATA
n=(iwidth*3*ichan)/1K
m=(3*3*ichan)/1K
p=min(n,m)
ndsp=p*ochan
ex: ichan=3,ochan=16,iwidth=768
ex: ichan=256,ochan=256,iwidth=192
ochan
Parallel implementation
weights
DSP 2
DSP p
DSP 1
DSP 2
DSP p
p=3
18x1K BRAM 2
18x1K BRAM 3
18x1K BRAM n
18x1K BRAM 4

## Slide 127
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM m
DSP 1
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM m
18x1K BRAM 1
striped row buffer
chained
accumulator
TDATA
TDATA
n=(iwidth*3*ichan)/1K
m=(3*3*ichan)/1K
p=min(n,m)
ndsp=p*ochan
ex: ichan=3,ochan=16,iwidth=768
ex: ichan=256,ochan=256,iwidth=192
ochan
Parallel implementation
weights
DSP 2
DSP p
DSP 1
DSP 2
DSP p
p=3
18x1K BRAM 2
18x1K BRAM 3
18x1K BRAM n
18x1K BRAM 4

## Slide 128
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM n
DSP
DSP
DSP
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM n
DSP
DSP
DSP
18x1K BRAM 1
18x1K BRAM 2
18x1K BRAM n
input buffer
weights
TDATA
TDATA

## Slide 129
18x1K BRAM 0
18x1K BRAM 1
18x1K BRAM n
DSP
DSP
DSP
18x1K BRAM 0
18x1K BRAM 1
18x1K BRAM n
DSP
DSP
DSP
18x1K BRAM 0
18x1K BRAM 1
18x1K BRAM m
input buffer
weights
TDATA
TDATA

## Slide 130
18x1K BRAM 0
18x1K BRAM 1
18x1K BRAM n
DSP
DSP
DSP
18x1K BRAM 0
18x1K BRAM 1
18x1K BRAM n
DSP
DSP
DSP
18x1K BRAM 0
18x1K BRAM 1
18x1K BRAM m
input buffer
weights
TDATA
TDATA

## Slide 131: AI application concept – thermal imaging CNN
MLX90640 IR Array Thermal Imaging Camera Module 32×24 Pixels 55° Field of View Camera with I2C Interface for Raspberry Pi/Arduino
32x24 calibrated FIR pixels, 14 bit precision, 32 fps
High precision non-contact temperature measurements
Intrusion / Movement detection
Presence detection / Person localization
Temperature sensing element for intelligent HVAC
Thermal Comfort sensor in automotive air conditioning control systems
Microwave ovens
Industrial temperature control of moving parts
Visual IR thermometers

## Slide 132: Example CNN tasks and training data
Gesture Recognition
Sign language
Occupancy Counting
Privacy preserving
Pose detection
Industrial Inspection
Anomaly Detection
PCB hot spot analysis
Animal health screening
Action Recognition
Human fall detection

## Slide 133: AI application prototype
Arty A7-100T
Artix-7
I2C @1MHz
10/100/1000 ethernet
32 fps
MLX90640
32x24 IR
prediction stream
server
MQTT
32 pkt/s
"accelerator" vs. hard real time
All parameters on chip using BRAM
Model evaluated entirely in FPGA fabric
Real time streaming pipeline

## Slide 134
9'
110 deg : 24' diameter
55 deg : 10' diameter